## Slide 1: Course11-“Advance”
Yahboom
Yahboom OMIBOX Tutorial

## Slide 2
Yahboom OMIBOX Tutorial
Learning
goals
Tencent
1
2
3
4
程序编程
5
Preparation
About code
Download
code
Experimental
phenomena

## Slide 3
1
Yahboom OMIBOX Tutorial
3. Learn how to control motor by programming
Learning goals
2. Learn about the PCA9685 drive chip pins connected to the Motor of Omibox programmable robot
1. The position of the Motor on the robot car

## Slide 4
2
Yahboom OMIBOX Tutorial
Preparation-1
As shown in the above picture, we circled the motors with two green wire frames, we circled the universal wheel with blue wire frames. We can control them by programming.

## Slide 5
2
Yahboom OMIBOX Tutorial
Preparation-2
According to the hardware manual, we can know that
Controlling the left motor forward is the Pin1 of the PCA9685.
Controlling the left motor back is the Pin2 of the PCA9685.
Controlling the right motor forward is the Pin15 of the PCA9685.
Controlling the right motor back is the Pin14 of the PCA9685.

## Slide 6
3
Yahboom OMIBOX Tutorial
About code
Please see the advance.ino file for this experimental procedure.

## Slide 7
4
Yahboom OMIBOX Tutorial
Download code
1.We need to open the code of this experiment: Advance.ino, click“√” under the menu bar to compile the code, and wait for the word "Done compiling " in the lower right corner, as shown in the figure below.
2. Click 【Tools】 --- 【Board】 -- we need to choose Arduino Uno. As shown in the figure below.

## Slide 8
4
Yahboom OMIBOX Tutorial
3.In the menu bar of Arduino IDE, we need to select 【Tools】---【Port】--- selecting the port that the serial number displayed by the device manager, as shown in the figure below.
4. After the selection is completed, you need to click “ → ”under the menu bar to upload the code to the Arduino UNO board. When the word “Done uploading” appears in the lower left corner, the code has been successfully uploaded to the Arduino UNO board, as shown in the figure below.
Download code

## Slide 9
5
Yahboom OMIBOX Tutorial
Experimental phenomena
After the program is uploaded, open the power of the robot car. After 2 seconds, Omibox will advance.

## Slide 10
Thank you!!!
Yahboom
Inspire Creativity Embrace Innovation